## Slide 1: Boolean Algebra
S.SADHISH PRABHU

## Slide 2: INTRODUCTION
1854: Logical algebra was published by George Boole  known today as “Boolean Algebra”
  It’s a convenient way and systematic way of expressing and analyzing the operation of logic circuits.
  1938: Claude Shannon was the first to apply Boole’s work to the analysis and design of logic circuits.

## Slide 3: Boolean Operations & Expressions
A symbol used to represent a logical quantity
.
The inverse of a variable and is indicated by a bar over the variable
A variable or the complement of a variable.
Variable
Complement
Literal

## Slide 4: Boolean Algebra
Section 01

## Slide 5: Boolean Algebra
A Boolean operator can be completely described using a truth table.
The AND operator is also known as a Boolean product.
The OR operator is the Boolean sum.
The NOT operation is most often designated by an overbar. It is sometimes indicated by a prime mark ( ‘ ) or an “elbow” ().

## Slide 6: Why Boolean Algebra?
#1
Digital computers contain circuits that implement Boolean functions.
#2
#3
#4
Now
The simpler that we can make a Boolean function, the smaller the circuit that will result.
Simpler circuits are cheaper to build, consume less power, and run faster than complex circuits.
With this in mind, we always want to reduce our Boolean functions to their simplest form.
There are a number of Boolean identities that help us to do this. .
Turning Point

## Slide 7: LAWS OF BOOLEAN ALGEBRA
This law states that ORing two or more variables and then ANDing the result with a single variable is equivalent to ANDing the single variable with each of the two or more variables and then ORing the products..
Commutative
Associative
Distributive
This law states that when ORing more than two variables, the result is the same regardless of the grouping of the variables
This law states that the order in which the variables are OR ed makes no difference..

## Slide 8
Rules of Boolean Algebra
Rules 1 through 9 will be viewed in terms of their application to logic gates.
Rules 10 through 12 will be derived in terms of the simpler rules and the laws previously discussed.
Idempotent law
Dominance law
Identity law
Identity law
Involution law
Complement law
Complement law
Idempotent law

## Slide 9: Rule 10 : A + AB = A
A + AB = A( 1 + B) Factoring (distributive law) = A . 1 Rule 2: (1 + B) = 1 = A Rule 4: A . 1 = A

## Slide 10: Rule 11

## Slide 11: Rule 12

## Slide 12: DEMORGAN'S THEOREMS
DeMorgan's first theorem is stated as follows:
The complement of a product of variables is equal to the sum of the complements of the variables.
Or
The complement of two or more ANDed variables is equivalent to the OR of the complements of the individual variables.
DeMorgan's second theorem is stated as follows:
The complement of a sum of variables is equal to the product of the complements of the variables.
Or
The complement of two or more ORed variables is equivalent to the AND of the complements of the individual variables

## Slide 13: Example #1
Example
  Simplify the following Boolean expression and note the Boolean or DeMorgan’s theorem used at each step. Put the answer in SOP form.
Solution
; Using DM law
; Rule` #9 & #DM LAW
; Theorem #9
; Rewritten without AND symbols and parentheses

## Slide 14: Example
Using Boolean algebra techniques, simplify this expression:
AB + A(B + C) + B(B + C)
Solution
Step 1: Apply the distributive law to the second and third terms in the expression, as follows:
AB + AB + AC + BB + BC
Step 2: Apply rule 7 (BB = B) to the fourth term.
AB + AB + AC + B + BC
Step 3: Apply rule 5 (AB + AB = AB) to the first two terms.
AB + AC + B + BC
Step 4: Apply rule 10 (B + BC = B) to the last two terms.
AB + AC + B
Step 5: Apply rule 10 (AB + B = B) to the first and third terms.
B+AC

## Slide 15: Example 2
  Solution
; DM law
; Rule 9
; DM law
; Rule 9
; Rewritten without AND symbols

## Slide 16: That’s all. Thank you very much! 
Any Questions?
.