## Slide 1: Module 3
DIGITAL ELECTRONICS

## Slide 2: Content
Number system
  Decimal
  Binary
  Octal
  Hexadecimal
Binary Arithmetic Operations
Boolean Algebra
Logic gates
Karnauph map POS and SOP

## Slide 3: Common Number system
Number systems | Base | Example
Decimal | 10 | (1934)10
Binary | 2 | (10101)2
Octal | 8 | (723)8
Hexadecimal | 16 | (A223)16

## Slide 4: The counting
Decimal | Binary | Octal | Hexadecimal
0 | 0 | 0 | 0
1 | 01 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
Decimal | Binary | Octal | Hexadecimal
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F
16 | 10000 | 20 | 10
17 | 10001 | 21 | 11
18 | 10010 | 22 | 12
19 | 10011 | 23 | 13
20 | 10100 | 24 | 14
21 | 10101 | 25 | 15

## Slide 5: Conversion
Decimal
Octal
Binary
Hexadecimal

## Slide 6: Decimal to binary Conversion
Divide by 2 and keep the remainder alive
Divide until the number is not divisible by 2
Collect the reminder and write from bottom to top

## Slide 7: Example
Convert (234)10 to binary
Ans:
11101010
Most Significant Bit
Least Significant Bit

## Slide 8: Decimal to Octal Conversion
Divide by 8 and keep the remainder alive
Divide until the number is not divisible by 8
Collect the reminder and write from bottom to top

## Slide 9: Example
Convert (234)10 to octal
Ans
(352)8

## Slide 10: Decimal to Hexadecimal Conversion
Divide by 16 and keep the remainder alive
Divide until the number is not divisible by 16
Collect the reminder and write from bottom to top

## Slide 11: Example
Convert (234)10 to hexadecimal
Ans
(EA)16

## Slide 12: Conversion
Decimal
Octal
Binary
Hexadecimal

## Slide 13: Binary to Decimal
  Multiply each bit by 2n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 14: Example
Convert (101011)2 to Decimal
Ans
43

## Slide 15: Octal to Decimal
  Multiply each bit by 8n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 16: Example
Convert (2347)8 to Decimal
Ans
1255

## Slide 17: Hexadecimal to Decimal
  Multiply each bit by 16n, where n is the “weight” of the bit
  The weight is the position of the bit, starting from 0 on the right
  Add the results

## Slide 18: Example
Convert (EAC2)16 to Decimal
Ans
60098

## Slide 19: Conversion
Decimal
Octal
Binary
Hexadecimal

## Slide 20: Octal to binary
  Convert each octal digit to a 3-bit equivalent binary representation
(176)8
Remember the BCD code : 4 – 2 – 1
Ans
0 0 1 1 1 1 1 1 0

## Slide 21: Hexadecimal to binary
  Convert each hexa digit to a 4-bit equivalent binary representation
(176)16
Remember the BCD code : 8 - 4 – 2 – 1
Ans
0 0 0 1 0 1 1 1 0 1 1 0

## Slide 22: Octal to hexadecimal / Hexadecimal to Octal
Use binary conversion as an intermediary